## Slide 1: 6LY CR-SCR specification Data sheet
01/12/2023

## Slide 2: Yanmar IMO teir III solution
Yanmar's IMO Tier III solution epitomizes excellence, harnessing the power of the compact, lightweight, and robust 6LY common rail 6-cylinder in-line engine, available in 400 and 440 mHp variants. Crafted with precision in-house, this integrated system incorporates an advanced Selective Catalytic Reduction (SCR) system, meticulously designed to comply with the latest MARPOL IMO III regulations.
Our Tier III solution is a testament to Yanmar's commitment to delivering the highest quality. It has undergone thorough certification by DNV, ensuring that it not only meets but exceeds industry standards.
6LY CR x SCR
50L Adblue Tank
150L Adblue Tank
SCR unit
Optional mixing elbow

## Slide 3: Technical Data
Item | Operating parameter/ requirements /specs | 
Engine | Yanmar 6LY CR | 
Supported power range | 6LY400 | 6LY440
Max output at cranckshaft (kW) | 294 kW@3300 rpm | 324kW@3300 rpm
Fuel | Max allowable sulfur content 500 ppm. EN590 & ASTM D975. | 
Weight (Engine+SCR) (kg) | 668 kg (DEF Tank not included) | 
SCR Operation Conditions (Exhaust temperatures °C) | Texh min = 220°C is the min exhaust gas temp at the inlet of the SCR chamber for reductant injection. Texh max = 600°C is the max exhaust gas temp at the inlet of the SCR chamber. | 
Max exhaust back pressure (kPa) | Pmax = pressure 30 kPa. | 
Power supply requirements (Vdc) | 24Vdc. 24Vdc, Tamb ≤ -12°C. | 
SCR chambers and catalyst | The SCR unit: 4x Ø13” x 4” catalysts, arranged as 2x HTS4 catalysts and 2x HTS3 catalysts. | 
6LY CR x SCR

## Slide 4: Technical Data
Item | Operating parameter/ requirements /specs
Reductant | Diesel Exhaust Fluid (DEF) 32.5%. According to AUS32 and ISO 22241. Consumption : at max load 3%.
Exhaust emission Compliance limit (g/kWh) | 0.42/2.0 g/kWh
Reductant injection system | DEF Injector
 | DEF Pump
 | SCR ECU
Adblue tank | 50L DEF Tank (plastic) (10kg)
 | 150L DEF Tank (SS) (71.5kg)
NOx sensors | Smart NOx Sensor
Temperature sensor | Measures SCR inlet exhaust gas temperature
Back pressure sensor | Measures exhaust gas back pressure
6LY CR x SCR

## Slide 5: System overview
6LY CR x SCR

## Slide 6
1- Catalyst | 11- SCR ECU | 21- Inlet
2- Mixer | 12- Adblue pump | 22- Backflow
3- Exhaust duct pipe (not included) | 13- Inlet NOx sensor | 23- Outlet
4- Adblue tank | 14- Backpressure sensor inlet 1 | 24- Adblue Backflow port
5- Sensor's bracket | 15- Temperature sensor | 25- Adblue feed port
6- Mixing elbow (optional) | 16- Backpressure sensor inlet 2 | 26- Connector SCR ECU
7- Adblue injector | 17- Outlet NOx sensor | 27- Sea water connection
8- NOx sensor 1 | 18- Interface Adblue connector | 28- heating inlet/outlet
9- NOx sensor 2 | 19- Interface coolant connector | 
10- Differential back pressure sensor | 20- Interface coolant connector | 
Front side | 
Back side | 
Optional | 
System overview
6LY CR x SCR